## Slide 1: ARM Architecture & Instruction Set
Subhasis Bhattacharjee

## Slide 2: ARM Features
ARM: Advanced RISC Machines
Most popular category of processors
  ARM 7(1995): ipod
  ARM 9(1997): Benq, sony erricson
  ARM 11(2003): Apple iphone, Nokia N93
  90% of the 32-bit embedded system uses ARM
ARM 32bit and above:
  Reasonably powerful
  Low power consumption
  Useful in battery operated devices.
ARM processor family share a common set of instructions.

## Slide 3: ARM Architecture
The ARM is a Reduced Instruction Set Computer (RISC) system and includes the attributes similar to that type of system:
A large array of uniform registers.
A load/store model of data-operations can only operate on registers and not directly on memory.
A uniform ﬁxed length instruction (32-bit).
A small number of addressing modes with all load/store addresses being determined from registers and instruction ﬁelds only.
Notes: A load/store model of data-operations can only operate on registers and not directly on memory. This requires that all data be loaded into registers before an operation can be preformed, the result can then be used for further processing or stored back into memory.

## Slide 4: ARM Architecture (additional features)
In addition ARM provides a number of additional features which are deviating from RISC:
Inline Barrel Shifter: h/w which allows multiple bit shifting very efficiently in a single clock cycle.
Auto-increment and Auto-decrement addressing modes to improve the operation of program loops.
Conditional execution of instructions to maximize execution throughput.
Configuration in Thumb Mode, operating over a subset of ARM instructions in 16 bit mode.

## Slide 5: ARM Block Diagram

## Slide 6: Registers
The ARM has a total of 37 registers.
  30 General purpose registers (over various modes), 1 program counter
  6 Status Registers
The general purpose registers can be used to handle 8-bit bytes, 16-bit half-words1, or 32-bit words.
R13 - Stack Pointer, R14 -Link Register (Return Address), and R15 -Program Counter
There are also one or two status registers depending on which mode the processor is in:
  Current Processor Status Register (CPSR) : information about the current status of the processor (including its current mode).
  Saved Processor Status Register (SPSR) : information on the processors state before changing mode, i.e., the processor status just before an exception
Structure of the Processor Status Registers

## Slide 7: ARM Machine Model
Memory (Von Neumann Architecture)
Register
Abbrv.
Name
r11
fp
frame pointer
r12
ip
intra-procedure-call scratch register
r13
sp
stack pointer
r14
lr
link register
r15
pc
program counter

## Slide 8: ARM Processor Modes
ARM supports the seven processor modes:
  Mode changes can be made under software control, or by external interrupts or exception processing.
  Privileged modes have full access to system resources.
  System mode is not entered by any exception

## Slide 9: User Mode
Most application programs execute in User mode.
  Registers: R0-R15
  R13 - Stack Pointer, R14 -Link Register (Return Address), and R15 -Program Counter
  One Status Register: CPSR
Structure of the Processor Status Registers
<cc> (Condition code) Mnemonics

## Slide 10: Generic Format
Generic Format
cond → instruction condition (eq, ne, … )
type → instruction type
cond
32
29
type
27
28
4
2

## Slide 11: ARM Instruction Encoding
cond
32
29
type
27
28
4
2
I
26
4
shifter operand/
Immediate/reg
25
22
S
21
4
rs
20
17
rd
4
16
13
12
12
1
opcode
cond → instruction condition (eq, ne, … )
type → instruction type (00: data processing, 01: Memory instruction, 10: branch )
I → Immediate bit, if I=0, second source operand is register
opcode → Instruction code
S → 'S' suffix bit (for setting the condition codes in CPSR)
rs, rd → source register, destination register

## Slide 12: ARM programmer model
The state of an ARM system is determined by the content of visible registers and memory.
A user-mode program can see 15 32-bit general-purpose registers (R0-R14), program counter (PC) and CPSR.
Instruction set defines the operations that can change the state.

## Slide 13: Memory system
Memory is a linear array of bytes addressed from 0 to 232-1
Word, half-word, byte
Little-endian
00
10
20
30
FF
FF
FF
00
00
00
0x00000000
0x00000001
0x00000002
0x00000003
0x00000004
0x00000005
0x00000006
0xFFFFFFFF
0xFFFFFFFE
0xFFFFFFFD

## Slide 14: ARM programmer model
00
10
20
30
FF
FF
FF
00
00
00
0x00000000
0x00000001
0x00000002
0x00000003
0x00000004
0x00000005
0x00000006
0xFFFFFFFF
0xFFFFFFFE
0xFFFFFFFD
R0 | R1 | R2 | R3
R4 | R5 | R6 | R7
R8 | R9 | R10 | R11
R12 | R13 | R14 | PC

## Slide 15: Instruction set
ARM instructions are all 32-bit long (except for Thumb mode). There are 232 possible machine instructions. Fortunately, they are structured.

## Slide 16: Features of ARM instruction set
Load-store architecture
3-address instructions
Conditional execution of every instruction
Possible to load/store multiple registers at once
Possible to combine shift and ALU operations in a single instruction

## Slide 17: Instruction set
Data processing
Data movement
Flow control

## Slide 18: Data processing
They are move, arithmetic, logical, comparison and multiply instructions.
Most data processing instructions can process one of their operands using the barrel shifter.
General rules:
  All operands are 32-bit, coming from registers or literals.
  The result, if any, is 32-bit and placed in a register (with the exception for long multiply which produces a 64-bit result)
  3-address format

## Slide 19: Instruction set
MOV<cc><S> Rd, <operands>
MOVCS R0, R1 @ if carry is set
@ then R0:=R1
MOVS R0, #0 @ R0:=0
@ Z=1, N=0
@ C, V unaffected

## Slide 20: Conditional execution
Almost all ARM instructions have a condition field which allows it to be executed conditionally.
movcs R0, R1

## Slide 21: Register movement
MOV R0, R2 @ R0 = R2
MVN R0, R2 @ R0 = ~R2
move negated
immediate,register,shift

## Slide 22: Addressing modes
Register operands
ADD R0, R1, R2
Immediate operands
ADD R3, R3, #1 @ R3:=R3+1
AND R8, R7, #0xff @ R8=R7[7:0]
a literal; most can be represented
by (0..255)x22n 0<n<12
a hexadecimal literal
This is assembler dependent syntax.

## Slide 23: Shifted register operands
One operand to ALU is routed through the Barrel shifter. Thus, the operand can be modified before it is used. Useful for fast multipliation and dealing with lists, table and other complex data structure. (similar to the displacement addressing mode in CISC.)
Some instructions (e.g. MUL, CLZ, QADD) do not read barrel shifter.

## Slide 24: Shifted register operands

## Slide 25: Logical shift left
MOV R0, R2, LSL #2 @ R0:=R2<<2
@ R2 unchanged
Example: 0…0 0011 0000
Before R2=0x00000030
After R0=0x000000C0
R2=0x00000030
C
0
register

## Slide 26: Logical shift right
MOV R0, R2, LSR #2 @ R0:=R2>>2
@ R2 unchanged
Example: 0…0 0011 0000
Before R2=0x00000030
After R0=0x0000000C
R2=0x00000030
C
0
register

## Slide 27: Arithmetic shift right
MOV R0, R2, ASR #2 @ R0:=R2>>2
@ R2 unchanged
Example: 1010 0…0 0011 0000
Before R2=0xA0000030
After R0=0xE800000C
R2=0xA0000030
MSB
register
C

## Slide 28: Rotate right
MOV R0, R2, ROR #2 @ R0:=R2 rotate
@ R2 unchanged
Example: 0…0 0011 0001
Before R2=0x00000031
After R0=0x4000000C
R2=0x00000031
register

## Slide 29: Rotate right extended
MOV R0, R2, RRX @ R0:=R2 rotate
@ R2 unchanged
Example: 0…0 0011 0001
Before R2=0x00000031, C=1
After R0=0x80000018, C=1
R2=0x00000031
register
C
C

## Slide 30: Shifted register operands

## Slide 31: Shifted register operands

## Slide 32: Shifted register operands
It is possible to use a register to specify the number of bits to be shifted; only the bottom 8 bits of the register are significant.
@ array index calculation
ADD R0, R1, R2, LSL R3 @ R0:=R1+R2*2R3
@ fast multiply R2=35xR0
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’

## Slide 33: Multiplication
MOV R1, #35
MUL R2, R0, R1
or
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’

## Slide 34: Shifted register operands

## Slide 35: Encoding data processing instructions
cond
0 0
operand 2
#
opcode
S
Rn
Rd
31
28
27
26
25
24
21
20
19
16
15
12
1
1
0
destination register
first operand register
set condition codes
arithmetic/logic function
8-bit immediate
1
25
1
1
8
7
0
#rot
Rm
1
1
7
6
5
4
3
0
#shift
Rm
0
25
1
1
8
7
6
5
4
3
0
Rs
Sh
0
1
0
Sh
immediate alignment
immediate shift length
shift type
second operand register
register shift length

## Slide 36: Arithmetic
Add and subtraction

## Slide 37: Arithmetic
ADD R0, R1, R2 @ R0 = R1+R2
ADC R0, R1, R2 @ R0 = R1+R2+C
SUB R0, R1, R2 @ R0 = R1-R2
SBC R0, R1, R2 @ R0 = R1-R2-!C
RSB R0, R1, R2 @ R0 = R2-R1
RSC R0, R1, R2 @ R0 = R2-R1-!C
3-5=3+(-5) → sum<=255 → C=0 → borrow
5-3=5+(-3) → sum > 255 → C=1 → no borrow
3
0
127
-128
-1
255
128
127
0
-5

## Slide 38: Arithmetic

## Slide 39: Arithmetic

## Slide 40: Setting the condition codes
Any data processing instruction can set the condition codes if the programmers wish it to
64-bit addition
ADDS R2, R2, R0
ADC R3, R3, R1
R1
R0
R3
R2
R3
R2
+

## Slide 41: Logical

## Slide 42: Logical
AND R0, R1, R2 @ R0 = R1 and R2
ORR R0, R1, R2 @ R0 = R1 or R2
EOR R0, R1, R2 @ R0 = R1 xor R2
BIC R0, R1, R2 @ R0 = R1 and (~R2)
bit clear: R2 is a mask identifying which
bits of R1 will be cleared to zero
R1=0x11111111 R2=0x01100101
BIC R0, R1, R2
R0=0x10011010

## Slide 43: Logical

## Slide 44: Comparison
These instructions do not generate a result, but set condition code bits (N, Z, C, V) in CPSR. Often, a branch operation follows to change the program flow.

## Slide 45: Comparison
CMP R1, R2 @ set cc on R1-R2
CMN R1, R2 @ set cc on R1+R2
TST R1, R2 @ set cc on R1 and R2
TEQ R1, R2 @ set cc on R1 xor R2
compare
compare negated
bit test
test equal

## Slide 46: Comparison

## Slide 47: Multiplication

## Slide 48: Multiplication
MUL R0, R1, R2 @ R0 = (R1xR2)[31:0]
Features:
  Second operand can’t be immediate
  The result register must be different from the first operand
  Cycles depends on core type
  If S bit is set, C flag is meaningless
See the reference manual (4.1.33)

## Slide 49: Multiplication
Multiply-accumulate (2D array indexing)
MLA R4, R3, R2, R1 @ R4 = R3xR2+R1
Multiply with a constant can often be more efficiently implemented using shifted register operand
MOV R1, #35
MUL R2, R0, R1
or
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’

## Slide 50: Multiplication

## Slide 51: Multiplication

## Slide 52: Flow control instructions
Determine the instruction to be executed next
pc-relative offset within 32MB

## Slide 53: Flow control instructions
Branch instruction
B label
…
label: …
Conditional branches
MOV R0, #0
loop: …
ADD R0, R0, #1
CMP R0, #10
BNE loop

## Slide 54: Branch conditions

## Slide 55: Branches

## Slide 56: Branch and link
BL instruction save the return address to R14 (lr)
BL sub @ call sub
CMP R1, #5 @ return to here
MOVEQ R1, #0
…
sub: … @ sub entry point
…
MOV PC, LR @ return

## Slide 57: Branch and link
BL sub1 @ call sub1
…
sub1: STMFD R13!, {R0-R2,R14}
BL sub2
…
LDMFD R13!, {R0-R2,PC}
sub2: …
…
MOV PC, LR
use stack to save/restore the return address and registers

## Slide 58: Conditional execution
CMP R0, #5
BEQ bypass @ if (R0!=5) {
ADD R1, R1, R0 @ R1=R1+R0-R2
SUB R1, R1, R2 @ }
bypass: …
CMP R0, #5
ADDNE R1, R1, R0
SUBNE R1, R1, R2
Rule of thumb: if the conditional sequence is three instructions
or less, it is better to use conditional execution than a branch.
smaller and faster

## Slide 59: Conditional execution
if ((R0==R1) && (R2==R3)) R4++
CMP R0, R1
BNE skip
CMP R2, R3
BNE skip
ADD R4, R4, #1
skip: …
CMP R0, R1
CMPEQ R2, R3
ADDEQ R4, R4, #1

## Slide 60: Data transfer instructions
Move data between registers and memory
Three basic forms
  Single register load/store
  Multiple register load/store
  Single register swap: SWP(B), atomic instruction for semaphore

## Slide 61: Single register load/store

## Slide 62: Single register load/store
No STRSB/STRSH since STRB/STRH stores both
signed/unsigned ones

## Slide 63: Single register load/store
The data items can be a 8-bit byte, 16-bit half-word or 32-bit word. Addresses must be boundary aligned. (e.g. 4’s multiple for LDR/STR)
LDR R0, [R1] @ R0 := mem32[R1]
STR R0, [R1] @ mem32[R1] := R0
LDR, LDRH, LDRB for 32, 16, 8 bits
STR, STRH, STRB for 32, 16, 8 bits

## Slide 64: Addressing modes
Memory is addressed by a register and an offset.
LDR R0, [R1] @ mem[R1]
Three ways to specify offsets:
  Immediate
LDR R0, [R1, #4] @ mem[R1+4]
  Register
  LDR R0, [R1, R2] @ mem[R1+R2]
  Scaled register @ mem[R1+4*R2]
  LDR R0, [R1, R2, LSL #2]

## Slide 65: Addressing modes
Pre-index addressing (LDR R0, [R1, #4])
without a writeback
Auto-indexing addressing (LDR R0, [R1, #4]!)
Pre-index with writeback
calculation before accessing with a writeback
Post-index addressing (LDR R0, [R1], #4)
calculation after accessing with a writeback

## Slide 66: Pre-index addressing
LDR R0, [R1, #4] @ R0=mem[R1+4]
@ R1 unchanged
R0
R1
+
LDR R0, [R1, ]

## Slide 67: Auto-indexing addressing
LDR R0, [R1, #4]! @ R0=mem[R1+4]
@ R1=R1+4
LDR R0, [R1, ]!
R0
R1
+
No extra time; Fast;

## Slide 68: Post-index addressing
LDR R0, R1, #4 @ R0=mem[R1]
@ R1=R1+4
R0
R1
+
LDR R0,[R1],

## Slide 69: Comparisons
Pre-indexed addressing
LDR R0, [R1, R2] @ R0=mem[R1+R2]
@ R1 unchanged
Auto-indexing addressing
LDR R0, [R1, R2]! @ R0=mem[R1+R2]
@ R1=R1+R2
Post-indexed addressing
LDR R0, [R1], R2 @ R0=mem[R1]
@ R1=R1+R2

## Slide 70: Example

## Slide 71: Example

## Slide 72: Example

## Slide 73: Summary of addressing modes

## Slide 74: Summary of addressing modes

## Slide 75: Summary of addressing modes

## Slide 76: Summary of addressing modes

## Slide 77: Load an address into a register
Note that all addressing modes are register-offseted. Can we issue LDR R0, Table? The pseudo instruction ADR loads a register with an address
table: .word 10
…
ADR R0, table
Assembler transfer pseudo instruction into a sequence of appropriate instructions
sub r0, pc, #12

## Slide 78: Application
ADR R1, table
loop: LDR R0, [R1]
ADD R1, R1, #4
@ operations on R0
…
ADR R1, table
loop: LDR R0, [R1], #4
@ operations on R0
…
table
R1

## Slide 79: Multiple register load/store
Transfer a block of data more efficiently.
Used for procedure entry and exit for saving and restoring workspace registers and the return address
For ARM7, 2+Nt cycles (N:#words, t:time for a word for sequential access). Increase interrupt latency since it can’t be interrupted.
registers are arranged an in increasing order; see manual
LDMIA R1, {R0, R2, R5} @ R0 = mem[R1]
@ R2 = mem[r1+4]
@ R5 = mem[r1+8]

## Slide 80: Multiple load/store register
LDM load multiple registers
STM store multiple registers
suffix meaning
IA increase after
IB increase before
DA decrease after
DB decrease before

## Slide 81: Addressing modes

## Slide 82: Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
Rn
R1
R2
R3

## Slide 83: Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
Rn
R1
R2
R3

## Slide 84: Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
Rn
R3
R2
R1

## Slide 85: Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
Rn
R1
R2
R3

## Slide 86: Multiple load/store register
LDMIA R0, {R1,R2,R3}
or
LDMIA R0, {R1-R3}
R1: 10
R2: 20
R3: 30
R0: 0x10
addr | data
0x010 | 10
0x014 | 20
0x018 | 30
0x01C | 40
0x020 | 50
0x024 | 60
R0

## Slide 87: Multiple load/store register
LDMIA R0!, {R1,R2,R3}
R1: 10
R2: 20
R3: 30
R0: 0x01C
addr | data
0x010 | 10
0x014 | 20
0x018 | 30
0x01C | 40
0x020 | 50
0x024 | 60
R0

## Slide 88: Multiple load/store register
LDMIB R0!, {R1,R2,R3}
R1: 20
R2: 30
R3: 40
R0: 0x01C
addr | data
0x010 | 10
0x014 | 20
0x018 | 30
0x01C | 40
0x020 | 50
0x024 | 60
R0

## Slide 89: Multiple load/store register
LDMDA R0!, {R1,R2,R3}
R1: 40
R2: 50
R3: 60
R0: 0x018
addr | data
0x010 | 10
0x014 | 20
0x018 | 30
0x01C | 40
0x020 | 50
0x024 | 60
R0

## Slide 90: Multiple load/store register
LDMDB R0!, {R1,R2,R3}
R1: 30
R2: 40
R3: 50
R0: 0x018
addr | data
0x010 | 10
0x014 | 20
0x018 | 30
0x01C | 40
0x020 | 50
0x024 | 60
R0

## Slide 91: Example

## Slide 92: Example
LDMIA r0!, {r1-r3}

## Slide 93: Example
LDMIB r0!, {r1-r3}

## Slide 94: Application
Copy a block of memory
  R9: address of the source
  R10: address of the destination
  R11: end address of the source
loop: LDMIA R9!, {R0-R7}
STMIA R10!, {R0-R7}
CMP R9, R11
BNE loop

## Slide 95: Application
Stack (full: pointing to the last used; ascending: grow towards increasing memory addresses)
LDMFD R13!, {R2-R9} @ used for ATPCS
… @ modify R2-R9
STMFD R13!, {R2-R9}
mode | POP | =LDM | PUSH | =STM
Full ascending (FA) | LDMFA | LDMDA | STMFA | STMIB
Full descending (FD) | LDMFD | LDMIA | STMFD | STMDB
Empty ascending (EA) | LDMEA | LDMDB | STMEA | STMIA
Empty descending (ED) | LDMED | LDMIB | STMED | STMDA

## Slide 96: Example

## Slide 97: Swap instruction
Swap between memory and register. Atomic operation preventing any other instruction from reading/writing to that location until it completes

## Slide 98: Example

## Slide 99: Application
Process A
While (1) {
if (s==0) {
s=1;
}
}
// use the
// resource
Process B
While (1) {
if (s==0) {
s=1;
}
}
// use the
// resource
S=0/1
OS

## Slide 100: Software interrupt
A software interrupt instruction causes a software interrupt exception, which provides a mechanism for applications to call OS routines.

## Slide 101: Example

## Slide 102: Load constants
No ARM instruction loads a 32-bit constant into a register because ARM instructions are 32-bit long. There is a pseudo code for this.

## Slide 103: Immediate numbers
cond
0 0
operand 2
#
opcode
S
Rn
Rd
31
28
27
26
25
24
21
20
19
16
15
12
1
1
0
destination register
first operand register
set condition codes
arithmetic/logic function
8-bit immediate
1
25
1
1
8
7
0
#rot
Rm
1
1
7
6
5
4
3
0
#shift
Rm
0
25
1
1
8
7
6
5
4
3
0
Rs
Sh
0
1
0
Sh
immediate alignment
immediate shift length
shift type
second operand register
register shift length
encoding for
data processing
instructions
v=n ror 2r
n
r

## Slide 104: Load constants
Assemblers implement this usually with two options depending on the number you try to load.

## Slide 105: Load constants
Assume that you want to load 511 into R0
  Construct in multiple instructions
  mov r0, #256
  add r0, #255
  Load from memory; declare L511 .word 511
  ldr r0, L511 ldr r0, [pc, #0]
Guideline: if you can construct it in two instructions, do it; otherwise, load it.
The assembler decides for you
ldr r0, =255 mov r0, 255
ldr r0, =511 ldr r0, [pc, #4]

## Slide 106: PC-relative modes
encoding for
data transfer
instructions
Impossible to use
direct addressing

## Slide 107: PC-relative addressing
main:
MOV R0, #0
ADR R1, a @ add r1, pc, #4
STR R0, [R1]
SWI #11
a: .word 100
.end
PC
fetch
decode
exec
fetch
decode
exec
fetch
decode
exec

## Slide 108: Instruction set