## Slide 1: Outline
Performance Metrics

## Slide 2: Measuring Performance
What do we mean by the performance of a processor ?
  ANSWER : Almost nothing
What should we ask instead ?
  What is the performance with respect to a given program or a set of programs ?
  Performance is inversely proportional to the time it takes to execute a program

## Slide 3: Computing the Time a Program Takes
CPI → Cycles per instruction
f → frequency (cycles per second)

## Slide 4: The Performance Equation
IPC → 1/CPI (Instructions per Cycle)
What are the units of performance ?
  ANSWER : arbitrary

## Slide 5: Number of Instructions (#insts)
Note that these are dynamic instructions
  NOT static instructions
A smart compiler can reduce the number of executed instructions
Static Instruction: The binary or executable of a program, contains a list of static instructions.
Dynamic Instruction: A dynamic instruction is a running instance of a static instruction, which is created by the processor when an instruction
enters the pipeline.

## Slide 6: Number of Instructions(#insts) – 2
Dead code removal
  Often programmers write code that does not determine the final output
  This code is redundant
  It can be identified and removed by the compiler
Function inlining
  Very small functions have a lot of overhead → call, ret instructions, register spilling, and restoring
  Paste the code of the callee in the code of the caller (known as inlining)

## Slide 7: Computing the CPI
CPI for a single cycle processor = 1
CPI for an ideal pipeline(no hazards)
  Assume we have n instructions, and k stages
  The first instruction enters the pipeline in cycle 1
  It leaves the pipeline in cycle k
  The rest of the (n-1) instructions leave in the next (n-1) consecutive cycles

## Slide 8: Computing the Maximum Frequency
Let the maximum amount of time that it takes to execute any instruction be :
  tmax (also known as algorithmic work)
Minimum clock cycle time of a single cycle pipeline → tmax
In the case of a pipeline, let us assume that all the pipeline stages are balanced
Time per stage → tmax / k

## Slide 9: Maximum Frequency - II
Let the latch delay be l
We thus have :
The minimum cycle time (1/f) is equal
to tstage . Let us thus, assume that
our cycle time is as low as possible.

## Slide 10: Performance of an Ideal Pipeline
Let us assume that the number of instructions are a constant

## Slide 11: Optimal Number of Pipeline Stages
k is inversely proportional to
k is proportional to

## Slide 12: Implications
As we increase the latch delay, we should have less pipeline stages
  We need to minimise the time wasted in accessing latches
As we increase the amount of algorithmic work, we require more pipeline stages for ideal performance
  More pipeline stages help distribute the work better, and increase the overlap across instructions

## Slide 13: Implications - II
As the number of instructions tends to ∞, the number of ideal pipeline stages also tends to ∞
  The higher startup time gets amortized in the long run

## Slide 14: A Non-Ideal Pipeline
Our ideal CPI (CPIideal = 1) is 1
However, in reality, we have stalls
Let us assume that the stall rate is a function of the program, and its nature of dependences

## Slide 15: Non-Ideal Pipeline - II
Let us assume that the stall penalty is proportional to the number of pipeline stages
Both these assumptions are strictly not correct. They are being used to make a coarse grained mathematical model.
CPI = (n+k-1)/n + rck
  r → stall rate, c → constant of proportionality

## Slide 16: Mathematical Model

## Slide 17: Mathematical Model - II

## Slide 18: Implications
For programs with a lot of dependences (high value of r) → Use less pipeline stages
For a pipeline with forwarding → c is smaller (than a pipeline that just has interlocks)
  It requires a larger number of pipeline stages for optimal performance

## Slide 19: Implications
The optimal number of pipeline stages is directly proportional to √(tmax / l)
  This ratio is not significantly changing across technologies.
  This explains why the number of pipline stages has remained more or less constant for the last 5-10 years

## Slide 20: Example
Example Consider two programs that have the following characteristics.
Program 1 |  | Program 2 | 
Instruction Type | Fraction | Instruction Type | Fraction
loads | 0.4 | loads | 0.3
Branches | 0.2 | Branches | 0.1
ratio(taken branches) | 0.5 | ratio(taken branches) | 0.4

## Slide 21: Example

## Slide 22: Performance, Architecture, Compiler
P
f
IPC
Architecture
Technology
Architecture
Compiler

## Slide 23
THE END