## Slide 1: Sequential Logic
Subhasis Bhattacharjee

## Slide 2: Sequential Networks
Memory / Time steps
Clock
Memory: Flip flops
Specification: Finite State Machines
Implementation: Excitation Tables
xi
yi
si
yi=fi(St,X)
sit+1=gi(St,X)
Notes: A combinational logic cannot have some sort of feedback loop where the output of a logic is also the input of it. A sequential network on the other hand can have this feature.

## Slide 3: Memory Devices
Memory Storage
Latches
Flip-Flops
  SR, D, T

## Slide 4: SR (Set/Reset) Latch
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1

## Slide 5: SR Latch Analysis
  S = 1, R = 0: then Q = 1 and Q = 0
  S = 0, R = 1: then Q = 0 and Q = 1

## Slide 6: SR Latch Analysis
  S = 1, R = 0: then Q = 1 and Q = 0
  S = 0, R = 1: then Q = 0 and Q = 1

## Slide 7: SR Latch Analysis
  S = 0, R = 0: then Q = Qprev
  S = 1, R = 1: then Q = 0 and Q = 0

## Slide 8
S
R
y
Q
Q = (R+y)’
y = (S+Q)’

## Slide 9: SR Latch Analysis
  S = 0, R = 0: then Q = Qprev and Q = Qprev (memory!)
  S = 1, R = 1: then Q = 0 and Q = 0 (invalid state: Q ≠ NOT Q)

## Slide 10: SR Latch Symbol
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1 (S = 1, R = 0, Q = 1)
  Reset: Make the output 0 (S = 0, R = 1, Q = 0)
Must do something to avoid
invalid state (when S = R = 1)

## Slide 11: D Latch
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1, D passes through to Q (the latch is transparent)
  When CLK = 0, Q holds its previous value (the latch is opaque)
Avoids invalid case when Q ≠ NOT Q

## Slide 12: D Latch Internal Circuit

## Slide 13: D Latch Internal Circuit

## Slide 14: D Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered device because it is activated on the clock edge

## Slide 15: D Flip-Flop Internal Circuit
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent, L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent, L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q

## Slide 16: D Flip-Flop vs. D Latch

## Slide 17: D Flip-Flop vs. D Latch

## Slide 18: D Flip-Flop (Delay)
D
CLK
Q
Q’
Id D Q(t) Q(t+1)
0 0 0 0
1 0 1 0
2 1 0 1
3 1 1 1
Characteristic Expression
Q(t+1) = D(t)
0 0 1
1 0 1
PS
D
0 1
State table
NS= Q(t+1)

## Slide 19: Sequential Modules: Introduction
Slice operation bitwise
Perform process in a series of time
Advantage:
  Cheaper hardware
  Fit for FPGA architecture
  Pipelining for excellent throughput
Disadvantage: Longer latency

## Slide 20: Serial Adder: Perform serial bit-addition
a0 b0
a3 b3
cin
cout
s0
s3
Serial
Adder
a
b
sum
si
ai
bi
At time i, read ai and bi. Produce si and ci+1
Internal state stores ci. Carry bit c0 is set as cin

## Slide 21
Serial Adder using D F-F
D
Q
Q’
Clk
si
ai
bi
C1
C1
D
Feed ai and bi and generate si at time i.
Where is ci and ci+1?

## Slide 22: Serial Adder using a D Flip-Flop
id | ai | bi | ci | ci+1 | si
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 1
D=ci+1
Q=ci

## Slide 23
D
Q
Q’
Clk
si
ai
bi
ci
Serial Adder using a D Flip-Flop
Logic Diagram

## Slide 24: Serial Adder using an SR Flip-Flop Excitation Table
id | ai | bi | ci (Q) | ci+1 | S | R
0 | 0 | 0 | 0 | 0 | 0 | -
1 | 0 | 0 | 1 | 0 | 0 | 1
2 | 0 | 1 | 0 | 0 | 0 | -
3 | 0 | 1 | 1 | 1 | - | 0
4 | 1 | 0 | 0 | 0 | 0 | -
5 | 1 | 0 | 1 | 1 | - | 0
6 | 1 | 1 | 0 | 1 | 1 | 0
7 | 1 | 1 | 1 | 1 | - | 0
SR generate ci+1
Q=ci

## Slide 25
0 0 0 1 -
1 1 0 1 -
PS
inputs
00 01 10 11
State table
Q(t+1)
SR
S
0 0 1 0
0 - - -
ai
bi
ci
R
- - 0 -
1 0 0 0
ai
bi
ci
0
1
PS
NS
0 1
0 - 1 0
0 1 - 0
Q(t+1)
Q(t)
Excitation table
Excitation Table of SR Flip-Flop

## Slide 26
ai
S
R
Q
Q’
si
Clk
ci
bi
ai
bi
S = aibi
R = ai’bi’
Serial Adder using an SR Flip-Flop
Logic Diagram

## Slide 27
Multiplication using Serial Addition
a2 a1 a0
b2 b1 b0
x
a2b0 a1b0 a0b0
a2b1 a1b1 a0b1
a2b1 a1b1 a0b1
+
m0
m1
0 1 1
1 0 1
x
0 1 1
+
0 0 0
0 1 1
0 1 1 1 1
3 X 5 = 15
For m=AxB, set m(0)=0
At time i, perform m(i+1)=m(i)+Abi2i

## Slide 28: Standard Sequential Modules
Register
Shift Register
Counter

## Slide 29: Register

## Slide 30: We Will Study Rest of the Topics Later on

## Slide 31: Shift Register

## Slide 32: Counter

## Slide 33: Counter: Applications
Program Counter
Address Keeper: FIFO, LIFO
Clock Divider
Sequential Machine

## Slide 34: Counter
Modulo-n Counter
Modulo Counter (m<n)
Counter (a-to-b)
Counter of an Arbitrary Sequence
Cascade Counter

## Slide 35
Modulo-n Counter
LD
D
Q
TC
Q (t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= (Q(t)+1)mod n if LD = 0, CNT = 1 and CLR = 0
= Q (t) if LD = 0, CNT = 0 and CLR = 0
CNT
CLR
Clk
TC = 1 if Q (t) = n-1 and CNT = 1
= 0 otherwise

## Slide 36
Modulo-m Counter (m< n)
Given a mod 16 counter, construct
a mod-m counter (0 < m < 16) with AND, OR, NOT gates
m = 6
Q3 Q2 Q1 Q0
3 2 1 0
CLK
CLR
CNT
D3 D2 D1 D0
0 0 0 0
LD
Q2
Q0
X
Set LD = 1 when X = 1 and (Q3Q2Q1Q0) = (0101), ie m-1

## Slide 37
A 5-to-11 Counter
Q3 Q2 Q1 Q0
Clk
CLR
CNT
D3 D2 D1 D0
0 1 0 1 (a)
LD
Q3
Q0
X
Set LD = 1 when X = 1 and (Q3Q2Q1Q0) = b (in this case, 1011)
Counter (a-to-b)
Given a mod 16 counter, construct an a-to-b counter
(0 < a < b < 15)
Q1
(b)

## Slide 38
Given a mod 8 counter, construct
a counter with sequence 0 1 5 6 2 3 7
Q2 Q1 Q0
Clk
CLR
CNT
D2 D1 D0
LD
Q2’
Q0
X
Q2
Q0 Q1 Q0
Q0’
When Q = 1, load D = 5
When Q = 6, load D = 2
When Q = 3, load D = 7
Counter of an Arbitrary Sequence